## Slide 1
ANADOLOGIC
2024 - ...

## Slide 2
ANADOLOGIC
IP Portfolio

## Slide 3
ANADOLOGIC
REFERENCES

## Slide 4
PROJECT
FPGA-accelerated industrial inspection
Real-Time Defect Detection with AMD Kria KR260
Notes: 2

## Slide 5
OUTLINE
What we'll cover today
1
Problem
2
Solution & System Overview
3
Developing on Kria
4
Inference
5
Preprocessing
6
Our Model
7
Pipeline
8
Results & Conclusion

## Slide 6
PROBLEM
The Challenge
  Industrial lines need fast, accurate defect detection
  CPU: Bottleneck at preprocessing and AI inference
  GPU: High power + non-deterministic latency
Our Goal
  Fast & accurate detection: FPGA-based pipeline with deterministic latency
  No CPU bottleneck: Hardware pre-processing + DPU inference fully offloaded to PL
  No GPU power/latency issues: Kria KR260 gives low power, real-time deterministic processing
What are we solving?

## Slide 7
SOLUTION OVERVIEW
End-to-end defect detection on KR260
  One board does it all: capture on the PS, accelerate preprocessing and inference in the PL, then activate the actuator
Camera
GigE · Mono8
Capture
Aravis (PS)
Preprocess
v_multi_scaler (VVAS) (PL)
Inference
DPU B4096 (PL)
Actuator
OK / Defective

## Slide 8
SYSTEM OVERVIEW
How the system works

## Slide 9
CARTRIDGE CASE INSPECTOR
Scratch, dent, crack inspection

## Slide 10
DEVELOPING ON KRIA
Camera
OMRON SENTECH STC-MBS202POE
  Protocol: GigE Vision 2.1
  Pixel Format: Mono8
  Interface: Gigabit Ethernet (PoE)
Processing Unit
  SoM: Kria K26
    Zynq UltraScale+ MPSoC
      4× ARM Cortex-A53
      FPGA fabric (PL)
  Carrier Board: KR260
    Gigabit Ethernet, USB 3.0, DisplayPort
  OS/Environment: Ubuntu, PetaLinux
System Hardware

## Slide 11
DEVELOPING ON KRIA
https://www.amd.com/en/products/system-on-modules/kria/k26/kr260-robotics-starter-kit.html
Kria KR260 Robotics Starter Kit
  AMD Kria K26 SOM designed for edge AI, robotics and industrial applications
  Contains both ARM processors (PS) and FPGA fabric (PL), ZynqMP SoC
  Runs standard Ubuntu, no custom OS needed
  Low-power consumption, suitable for industrial environments
What is the Kria SOM?

## Slide 12
Legacy MPSoC Flow (static boot image flow)
  Bitstream baked into BOOT.bin and loaded at boot
  One OS per app
  Reboot to switch app
Kria SOM Flow (KV260, KR260)
  Bitstream not in boot image and loaded at runtime
  Single OS, multiple apps
  No reboot to switch app
DEVELOPING ON KRIA
Bitstream Management: Legacy vs Kria SOM
https://xilinx.github.io/kria-apps-docs/creating_applications/2022.1/build/html/docs/bitstream_management.html

## Slide 13
DEVELOPING ON KRIA
Producing the PL: Vivado Flow vs Vitis Flow
Vivado flow
  Hand-built block design in IP Integrator
  You wire every IP (DPU, scaler, VDMA) manually
  Maximum control, most manual effort
Vitis flow (our choice)
  Start from a base platform (AMD-provided or custom) + accelerator kernels
  The tool links the platform + accelerator kernels (e.g. DPU, multiscaler) automatically, no manual wiring
  Skips re-synthesizing the platform each iteration, only the kernel is synthesized
  Bottom line: we use the Vitis acceleration flow, less manual wiring and reusing the platform saves synthesis time

## Slide 14
DEVELOPING ON KRIA
Vitis Acceleration Flow
https://xilinx.github.io/kria-apps-docs/creating_applications/2022.1/build/html/docs/overview.html
  Platform + Accelerators → v++ --link → 3 output files
  Platform (.xpfm): KR260 base hardware design, two options:
    Use AMD provided platform (e.g. kv260_ispMipiRx_vcu_DP, kr260_pmod_gps)
    Create custom platform with Vivado
  Accelerators (.xo): PL kernels written in HLS or RTL
  v++ --link: combines platform + accelerators → generates .bit.bin + .xclbin + .dtbo

## Slide 15
DEVELOPING ON KRIA
Runtime Software Stack: XRT & ZOCL
  Load: overlay is activated at runtime via the Linux FPGA manager (xmutil loadapp) without a reboot
    .bit.bin → programs the PL fabric
    .dtbo → tells Linux what hardware appeared in PL
  Run: once active, the application drives the accelerators through XRT + ZOCL
    XRT (Xilinx Runtime): Software library running on PS (ARM) side that manages buffer allocation, DMA, kernel control
    ZOCL (Zynq OpenCL driver): Linux kernel driver that physically maps/drives the PL registers
    .xclbin → read by XRT for register maps + kernel metadata
Run Phase

## Slide 16
OUR IMPLEMENTATION
Custom FPGA overlay
  Custom FPGA overlay for Kria KR260 targeting real-time industrial defect detection
  Camera: OMRON SENTECH STC-MBS202POE — GigE Vision/ Mono8
  Platform: Minimal custom Vitis platform (clock/interrupt/AXI only, no extra fixed IP), built in Vivado
  Accelerators: DPU B4096 (Inference) + v_multi_scaler (HW preprocessing)
  Software stack: Ubuntu 22.04 / XRT 2.15 / Vitis AI 2.5 / VVAS 2.0 / GStreamer / Aravis
  Build flow: Vitis Acceleration Flow → v++ --link → .bit.bin + .xclbin + .dtbo
  Output: Binary defect classification — OK / Defective
Software Architecture of the Platform — Kria™ KV260 2022.1 documentation
Notes: 10

## Slide 17
INFERENCE
What is the DPU?
  Deep Learning Processing Unit: Xilinx's hardware IP for running neural network inference on the FPGA
  Runs our custom-trained defect detection model directly in PL, no CPU involved
  Comes in different sizes (architectures), B512 up to B4096
https://docs.amd.com/r/en-US/pg338-dpu/Core-Overview

## Slide 18
INFERENCE
What do B4096 and B3136 mean?
  The “B” number = peak operations per clock — what the convolution engine can do each cycle (1 MAC = 2 ops)
  B4096 = 4096 ops/clock; B3136 = 3136; B512 = 512. Bigger = more parallel MAC units
  Set by three parallelism factors: pixel (PP) × in-channel (ICP) × out-channel (OCP), × 2
  – B4096 = 8 × 16 × 16 × 2
– B3136 = 8 × 14 × 14 × 2
  More parallelism → higher throughput (more FPS) but more LUT / FF / BRAM / DSP
  A bigger DPU is faster but costs more PL resources — the budget problem on the next slides
Peak operations per clock
B512
512
B1024
1024
B2304
2304
B3136
3136
B4096
4096

## Slide 19
INFERENCE
Resource budget vs K26
https://docs.amd.com/r/en-US/pg338-dpu/Resource-Utilization
  We want a powerful DPU like B3136 or B4096 but BRAM isn't enough. What can we do?
DPUCZDX8G Architecture | LUT | Register | Block RAM | DSP
B512 | 26922 | 34543 | 72 | 118
B800 | 29721 | 41147 | 90 | 166
B1024 | 34074 | 48057 | 104 | 230
B1152 | 32169 | 47374 | 121 | 222
B1600 | 38418 | 58831 | 126 | 326
B2304 | 42127 | 68829 | 165 | 438
B3136 | 46714 | 79710 | 208 | 566
B4096 | 52161 | 98249 | 255 | 710
Table 1: Resources of Different DPUCZDX8G Architectures
Resource | K26 SOM | Description
System logic cells | 256,200 | Programmable logic cells for available
CLB flip-flops | 234,240 | Configurable logic block (CLB): Total number of flip-flops
CLB LUTs | 117,120 | Configurable logic block: Total number of look-up tables
Distributed RAM (Mb) | 3.5 | Distributed memory
Block RAM | 144 | Number of 36 Kb block RAMs
Block RAM (Mb) | 5.1 | Total block RAM memory footprint
UltraRAM blocks | 64 | 288 Kb dual-port, 72-bit-wide memory with error correction
DSP slices | 1,248 | 27 x 18 signed multiplier with 48-bit adder/accumulator
CMTs | 4 | Clock management tiles
Video Codec | 1 | H.264 and H.265 supported simultaneous encode/decode
HDIO | 69 | High-density I/O supports 1.2V to 3.3V rails
HPIO | 116 | High-performance I/O differential pairs supports 1.0V to 1.8V rails
GTH transceivers | 4 | Up to 12.5 Gb/s serial transceivers
Transceiver fractional PLLs | 8 | Specialized PLL used in high-speed serial communication transceivers
PCI Express | 1 | Controller for integrated PCIe that is in addition to the integrated controller for PCIe in the PS
https://docs.amd.com/r/en-US/ds987-k26-som/Programmable-Logic
Table 2: PL Resources
Notes: 12

## Slide 20
INFERENCE
The answer: URAM
  We can use URAM so that we can use a powerful DPU architecture
  Kria SOM has 64 URAM blocks available
  Configuring DPU to use URAM frees up BRAM for the scaler
DPUCZDX8G Architecture | LUT | Register | Block RAM | UltraRAM | DSP
B512 | 26767 | 34538 | 0 | 18 | 118
B800 | 29578 | 41153 | 0 | 40 | 166
B1024 | 33752 | 48093 | 0 | 26 | 230
B1152 | 31901 | 47797 | 0 | 44 | 222
B1600 | 38197 | 58859 | 0 | 56 | 326
B2304 | 41736 | 69604 | 0 | 60 | 438
B3136 | 46260 | 80079 | 0 | 64 | 566
B4096 | 51843 | 98567 | 0 | 68 | 710
Table 3: Resources of DPUCZDX8G using UltraRAM

## Slide 21
PRE-PROCESSING
Getting frames into the format the model expects
  A trained CNN expects a fixed input tensor — our ResNet-18 needs a set size, layout and value range, not the raw camera frame
  Color space conversion: the camera gives Mono8 (grayscale); the model needs a defined format and channel order (e.g. 3-channel BGR)
  Scaling (resize): the full frame (e.g. 1920×1080) is resized to the model input (e.g. 224×224)
  Normalization / quantization: pixel values are scaled to the INT8 range the DPU runs on
  On the CPU this is a bottleneck → we offload it to the v_multi_scaler in PL (next slide)
Raw frame
1920×1080 Mono8
Color
Convert
Resize
224×224
Quantize
INT8
DPU

## Slide 22
PRE-PROCESSING
What is VVAS / Multiscaler?
  VVAS (Vitis Video Analytics SDK): Xilinx's open-source framework providing GStreamer plugins and hardware kernels for video processing on FPGA
  v_multi_scaler: the HLS IP from VVAS that does hardware image preprocessing (resize, format conversion)
  Takes the load off the CPU, frees ARM cores for other tasks
  Inference runs through VART (Vitis AI Runtime), wrapped by the VVAS plugin
https://www.amd.com/en/developer/resources/vitis-video-analytics-sdk.html

## Slide 23
OUR MODEL
Computer Vision Tasks
Classification
“What is in the image?”
One label for the whole image (e.g. OK / Defective)
▶ Our task
Detection
“What and where?”
A bounding box + a class for each object
Segmentation
“Which pixels?”
A per-pixel class mask - the exact object shape
  We do binary classification: OK / Defective - one decision per frame

## Slide 24
OUR MODEL
Custom defect detection, from PyTorch to the DPU
  Model: ResNet-18 (PyTorch)
    Binary classification: OK / Defective
  From model to FPGA, Vitis AI 2.5 flow:
    Train: ResNet-18 in PyTorch (FP32)
    Quantize: Vitis AI 2.5 → INT8
    Compile: Vitis AI compiler → .xmodel for the DPU
    Deploy: Runs on DPU
https://xilinx.github.io/Vitis-AI/3.0/html/docs/workflow-model-deployment.html

## Slide 25
PIPELINE
Runtime architecture

## Slide 26
PIPELINE
Example GStreamer pipeline (VVAS)
gst-launch-1.0 -v \
aravissrc camera-name="Sentech-STC-MBS202POE" \
! queue \
! vvas_xmultisrc kconfig="/opt/xilinx/defect-detect/share/vvas/preprocess.json" \
! video/x-raw,format=BGR,width=224,height=224 \
! queue \
! vvas_xfilter kernels-config="/opt/xilinx/defect-detect/share/vvas/aiinference.json" \
! queue \
! kmssink driver-name=xlnx fullscreen-overlay=true
  aravissrc — GStreamer source plugin from Aravis, an open-source GigE Vision driver; pulls Mono8 frames from the camera into the pipeline
  vvas_xmultisrc — HW preprocessing (resize + color convert) on the v_multi_scaler, config set via preprocess.json
  vvas_xfilter — runs the ResNet-18 .xmodel on the DPU via VART, config set via aiinference.json; attaches the OK / Defective result as metadata
  kmssink — displays the frame on DisplayPort (Xilinx DRM/KMS driver)

## Slide 27
RESULT AND CONCLUSION
Resource Utilization

## Slide 28
RESULT AND CONCLUSION
Embedded World - 2026

## Slide 29
ANADOLOGIC
REFERENCES